Weekly Cleaning Routine

May Be Done More Often If Necessary.

USE ONLY WARM WATER & MILD DETERGENT.

Do Not Use Abrasive Cleaners or Cleaning Pads on Machine.

To Empty Bowl:

Drain Product Until Completely Empty.

Turn Off Power And Unplug Power Cord From Wall.

To Remove Faucet Assembly:

With Hand On Handle (5.04), Remove Handle Pin (5.05)

With Hand Under Faucet Assembly, Remove Handle (5.04)

With Finger Push Down On Tap Spring (5.06) & Tap Pin (5.07)

Wash Parts In Warm Cleaning Solution.

Rinse With Sanitizer.

To Loosen Empty Bowl:

Turn Off Power And Unplug Power Cord From Wall.

Unplug Lid Power Cord (1.05) And Remove Lid.

Clean Lids with Warm Cleaning Solution.

Rinse with Sanitizer.

Raise Bowl At Front Until Legs “Pop” Out.

Slowly Remove Bowl (5.01).

Remove Hard Plastic Bowl Bushing (5.10) At Front Of The Bowl.

Soak Bushing In Bowl of Warm Cleaning Solution For 10 Minutes.

Wash Bowl Out With Non Abrasive Cloth.

Rinse With Sanitizer.

To Remove Spiral & Gaskets:

Slowly Remove Spiral (2.00)

Remove Suction Cap (2.05) From Spiral (2.00).

Remove Bowl Gasket (3.02) At Back Of Freezing Cylinders.

Wash Parts With Warm Cleaning Solution.

Rinse With Sanitizer.

Weekly Cleaning Routine

May Be Done More Often If Necessary.

USE ONLY WARM WATER & MILD DETERGENT.

Do Not Use Abrasive Cleaners or Cleaning Pads on Machine.

To Remove Drip Trays:

Remove Grates (7.10).

Lift Drip Trays (7.09) Up and Out.

Clean With Warm Cleaning Solution.

Rinse With Sanitizer.

To Clean Base Unit:

Clean Freezing Cylinders & Condensation Pans (7.01) With Warm Cleaning Solution.

Wipe Down Rest of Base.

Sanitize Entire Base.

Note:

Allow To Dry Before Reassembly.

For Additional Help or Service Call:

Equipment Masters L.L.C.

Phone:(817-439-4458)

Fax :   (817-439-4854)

Monthly Condenser Cleaning Routine

May Be Done More Often If Necessary.

USE ONLY SOFT BRISTLE BRUSH.

Do Not Use Hard Bristle Brush on Condenser.

To Clean Condenser Unit:

Turn Off Machine And Unplug Power Cord From Wall.

Unscrew Side Panels.

Lift Off Side Panels.

Brush Entire Condenser Unit With Soft Brush Until All Dirt & Dust Is Removed.

Replace Side Panels.

Screw Into Place.

Attention:

A Dirty Condenser Can Cause Compressor Damage.

For Additional Help or Service Call:

Equipment Masters L.L.C.

Phone:(817-439-4458)

Fax :   (817-439-4854)

Machine Assembly

Inspect All Gaskets & Bushings Before Assembly.

MAKE SURE MACHINES IS UNPLUGGED BEFORE ASSEMBLY.

Discard And Replace Any Worn Or Broken Gasket.

Slide Bowl Gasket (3.02) To Back Of The Freezing Cylinder With Flat Side Flush Against Machine Base.

Insert Suction Cap Gasket (2.05) Completely Into Spiral (2.00).

Apply Lube Around Shaft Of Freezing Cylinder.

Slide Spiral (2.00) Back Onto Freezing Cylinder.

Turn Unto Spiral (2.00) Is Locked Into Place.

Slide Bowl (5.01) Back Onto Freezing Cylinder.

Gently Snap Bowl Legs Into Place, Will “Pop”.

Lube White O-Ring (5.08) and Lower Tap Gasket (5.09) on Tap Pin (5.07).

Machine Assembly

Inspect All Gaskets & Bushings Before Assembly.

MAKE SURE MACHINES IS UNPLUGGED BEFORE ASSEMBLY.

Balance Tap Spring (5.06) On Top Of Tap Pin (5.07)

Insert Both Into Bowl Spout Using Finger To Hold In Place.

Insert Handle (5.04) To Lock In Tap Pin (5.07) Continue Holding Handle.

Insert Handle Pin (5.05) To Everything In Place.

Check For Easy Up And Down Motion.

Place Lids On Top Of Bowl (5.01).

Plug In Lid Power Cord (1.05).

Insert Drip Tray (7.09) In Then Down.

Insert Grate (7.10) Into Drip Tray (7.09).

Plug Machine Power Cord (7.14) Into Wall.

For Additional Help or Service Call:

Equipment Masters L.L.C.

Phone:(817-439-4458)

Fax :   (817-439-4854)

Timer & Control Panel

Timer

Note:

The timer starts the night function of the machine.

How to Use Timer

- Switch on the Machine;

- See Picture 1 for time reference;

- Rotate timer till the white triangle is set to the right local time.  Please note AM – PM signs.

Do not relay on center Analog Clock,

just for display purpose only.

Without the correct time setting, the timer will not work properly.

- Push all night (Cold Drink Dispenser) segments outwards and all day (Slush Dispenser) segments inward.

- Do not turn off machine at night.

NOTE:

See Picture 2

Current time is 9:00 AM.   Machine will dispense Slush drinks from 7:00 AM to 11:00 PM.  Then from 11:01 PM to 6:59 AM will be a Cold Drink Dispenser.  Machine will not defrost product.

Control Panel Diagram

- Main Power Switch

- Lid Lights Switch

- Bowl 1 Freeze

- Bowl 2 Freeze

Note:

Bowl 1 Is Bowl Nears To Control Panel.

For Additional Help or Service Call:

Equipment Masters L.L.C.

Phone:(817-439-4458)

Fax :   (817-439-4854)

Weekly Maintenance Sign Off Sheet

MAKE SURE MACHINES IS UNPLUGGED.

| Date | Employee Name | Parts Replaced | Notes |
| --- | --- | --- | --- |

For Additional Help or Service Call:

Equipment Masters L.L.C.

Phone:(817-439-4458)

Fax :   (817-439-4854)